## Slide 1: iCatching
CDR Presentation
Tom Queen
Daniel Turner
Demetrius Zaibo

## Slide 2: Status: Frame
Kinematics Implemented
Error Sources:
  Rounding errors from using floats on a microcontroller
  Discrete time system
Doesn’t whack against frame sides or oscillate
  Boundary checks with hysteresis return
  Input dead-band before gripper will move
Motors are naff
  Can’t increase the system tension by any appreciable amount
  Steppers skip and spools slip
Demo!

## Slide 3: Status: Throwing
Motor inadequacy workaround: Clamps for all cables
  Went through various design iterations
Intention is to use a different motor for the pullback mechanism
  Same spool, but need a new spool to motor connection
Flow diagram for the control system is finished

## Slide 4: Status: Catching
Camera can reliably track from 4m away
  Customise input settings via QV4L2:
    Maxed out saturation & shifted hue by 45 degrees
    Turned off auto gain, auto white balance & auto exposure
    Manually adjust the brightness for the environment
  Colour threshold in OpenCV:
    Convert to HSV
    Average a number of pixels within the image
    Threshold using the average and an offset
Using a known object (a red tennis ball)
  Circle detection
  Ball size is proportional to distance away
Can catch!
  Demo

## Slide 5: Summary
Simulation suggests system should work
  Mechanical limitations are the most prominent source of bugs
Antagonistic control potential
  Bungee cord has non-linear elasticity
  Motors prevent actualisation
Catching system is 90% complete
  Need to attach and run tests with camera feedback
Throwback system is 40% complete
  More clamps needed
  Requires hardware assembly & software implementation still
    (and more testing!)

## Slide 6: Questions?